## Slide 1: PARKING SPACE DETECT
_Amanullah Tariq, Muazzam Ali and Deep Ganatra

## Slide 2: Content
TASK 1 : Parking area detection in 2D Image
KEY IDEA : Detect patterns in Parking area.
Results
TASK 2 : 2D – 3D Registration
KEY IDEA : Register known correspondence points
Ground plane detection and filtering
TASK 3 : Segmentation of objects and 2D-3D Mapping
Step 1 : Object Detection
Step 2 : Applying Supervised Learning
Step 3 : Combining 2D – 3D data

## Slide 3
TASK 1: Parking area detection in 2D Image
Detect parking area features in images (e.g., lines, corners, patterns…)
Generate a map of parking spaces.

## Slide 4
Applying Bilateral
Original Image
Notes: http://docs.opencv.org/doc/tutorials/imgproc/gausian_median_blur_bilateral_filter/gausian_median_blur_bilateral_filter.html
http://homepages.inf.ed.ac.uk/rbf/CVonline/LOCAL_COPIES/MANDUCHI1/Bilateral_Filtering.html

## Slide 5
Applying Bilateral
Bilateral Image

## Slide 6
Converting Image to Grey for easy processing

## Slide 7
Detecting Line Segments
Algorithm : Line Segment Detect (OpenCV 3.0).
Notes: http://docs.opencv.org/3.0-beta/modules/line_descriptor/doc/LSDDetector.html

## Slide 8
Categorising Lines on basis of Slopes

## Slide 9
Working with Lines at same slope

## Slide 10
Categorize lines at same slope, by length and threshold
Maxlinelength = length of most occurring lines (l)

## Slide 11
Calculating distance between mid-points of the lines

## Slide 12
Checking Aspect ratio
Aspect ratio =
0.4 < Aspect ratio for rectangle < 0.7

## Slide 13
Calculating perpendicular distance between lines
Notes: https://en.wikipedia.org/wiki/Distance_between_two_straight_lines

## Slide 14
Getting rectangle corner points
Desired points
Notes: Unit vector in direction of desired point, multiply by the distance is the new point.

## Slide 15
Rectangle plotted results

## Slide 16
TASK 2: 2D – 3D Registration

## Slide 17
TASK 2: 2D – 3D Registration
Manually detect the Correspondence points.
Compute a transformation of the 2D image and the 3D point cloud.

## Slide 18
3D PCD with Intensity of parking space

## Slide 19: Normalizing & Thresholding the Intensity values
Normalizing Intensities of each point (0 to 1)
= Maximum Intensity value in Point Cloud Data
= 0.5

## Slide 20: New Intensity value

## Slide 21
2D image and Point Cloud

## Slide 22
KEY IDEA : Register known correspondance points

## Slide 23: Correspondence points

## Slide 24
Transformation using Umeyama1 Algorithm
Least square estimation of the transformation parameters.
Single Value Decomposition of covariance matrix.
Notes: http://web.stanford.edu/class/cs273/refs/umeyama.pdf

## Slide 26
Ground plane detection and filtering
Notes: Reference:
http://pointclouds.org/documentation/tutorials/planar_segmentation.php
SACMODEL_PLANE - used to determine plane models. The four coefficients of the plane are its Hessian Normal form: [normal_x normal_y normal_z d]
seg.setModelType (pcl::SACMODEL_PLANE);
seg.setMethodType (pcl::SAC_RANSAC);
seg.setDistanceThreshold (3);

## Slide 27
RANSAC – Random Sample Consensus
Algorithm for robust model fitting
Select sample Set – Point Cloud Data
Computes Model - SACMODEL_PLANE
Computes inliers – Points in Plane
Repeats until sufficient confident.

## Slide 28
SACMODEL_PLANE 1
The four coefficients of the plane are its Hessian Normal form: [normal_x, normal_y, normal_z, d]
Notes: Reference:
http://pointclouds.org/documentation/tutorials/planar_segmentation.php
SACMODEL_PLANE - used to determine plane models. The four coefficients of the plane are its Hessian Normal form: [normal_x normal_y normal_z d]
seg.setModelType (pcl::SACMODEL_PLANE);
seg.setMethodType (pcl::SAC_RANSAC);
seg.setDistanceThreshold (3);

## Slide 29
Filtering out the plane using EXTRACT INDICES
Plane detected
Point cloud with Extract indices

## Slide 30: Task 3: Car Detection

## Slide 31: Task 3: Car Detection (Required)
Registration from previous task provides a segmentation of cars.
Use these point clouds as training examples to compute car features.
Implement a car detector.
Map Improvement.

## Slide 32: Task 3: Car Detection (Solution)
Object Detection
Clustering Methods
Identifying Threshold Values
Applying Supervised Learning
Logistic Regression
Combining 2D and 3D data
Matching
Drawing
Reference:
Logistics Regression
Notes: The binary logistic model is used to predict a binary response based on one or more predictor variables (features), making it a probabilistic classification model in the parlance of machine learning,[4] or a qualitative response/discrete choice model in the terminology of economics.

## Slide 33
Step 1: Object Detection

## Slide 34: Step 1: Object Detection
Clustering Methods
Euclidean Cluster Extraction
Region Growing Segmentation
Identifying Threshold
Manual feature(s) detection

## Slide 35: Euclidean Cluster Extraction
  Euclidean Cluster Extraction
Reference:
Euclidean Cluster Extraction
KD-Tree
Notes: http://www.pointclouds.org/documentation/tutorials/cluster_extraction.php

## Slide 36: Euclidean Custer Extraction
  Euclidean Cluster Extraction (Continue)
Reference:
Euclidean Cluster Extraction
KD-Tree
Blue objects are identified clusters
Notes: http://www.pointclouds.org/documentation/tutorials/cluster_extraction.php

## Slide 37
  Region Growing Segmentation
This algorithm merge the points that are close enough in terms of the smoothness constraint. Thereby, the output of this algorithm is the set of clusters, were each cluster is a set of points that are considered to be a part of the same smooth surface. The work of this algorithm is based on the comparison of the angles between the points normal.
Takes more time than Euclidean Cluster Extraction.
Reference:
Region Growing Segmentation

## Slide 38
  Region Growing Segmentation (Continue)

## Slide 39
  Region Growing Segmentation (Continue)
Reference:
Region Growing Segmentation
Blue objects are identified clusters

## Slide 40
  Comparison: Euclidean VS Region Growing
Euclidean
Region Growing
For our rest of the program we used Region Growing.

## Slide 41
Identifying Threshold Values (Manually)
Manually visualize all the clusters and saved them in a Excel sheet.
Attributes saved where
  Length ( y – value)
  Height ( z – value)
  Width ( x – value)
  Type ( Car / Not Car)
Result

## Slide 42: Problem(s)
Can we used the manually identified thresholds?
  Hard coded values can lead to big errors.
  What if truck comes and what if small car comes.
  If we have to hard code the threshold values then why we are writing so much code?
How to solve this problem?
  Supervised Learning.
Which supervised algorithm to use ?
  Small feature list.
  Only need to classify objects as Cars and Not Cars (binary)
  SVM, Linear , logistic regression etc.
Reference:
Liblinear
Notes: There are some large data for which with/without nonlinear mappings gives similar performances. Without using kernels, one can quickly train a much larger set via a linear classifier.
L2 uses Gaussians coefficients.
L1 uses Laplace coefficients.
L1 regularization does not give higher accuracy but may be slightly slower in training.

## Slide 43
Step 2: Applying Supervised Learning

## Slide 44: Step 2: Applying Supervised Learning
Process
Training
Prediction
Results
Output
Accuracy

## Slide 45
Process (Training & Prediction)
  Feature List as text file Model File/ learned function
.
Training
.
Predictor
Model File
Output (Classifying Clusters)
Map
Clusters

## Slide 46
Process (continue)
Training
  We use following solver or methods
    L1-regularized logistic regression
    L2-regularized L2-loss support vector classification (dual)
  Prediction
    Model
    Output
    Input
Reference:
Liblinear

## Slide 47: Process(Continue)
Reference:
Liblinear

## Slide 48: Results
Notes: SVM is implemented in the LibLinear library that we use

## Slide 49
Accuracy
  L1-regularized logistic regression
  L2-regularized L2-loss support vector classification (dual)
Notes: http://pointclouds.org/documentation/tutorials/region_growing_segmentation.php#region-growing-segmentation

## Slide 50: Step 3: Combining 2D and 3D

## Slide 51: What we will do next ?
Parking spots identified from 2D Image
Occupied Parking slots identified from PCD file
Final Map
(Parking and Vacant Spaces)

## Slide 52: Step 3: Combining 2D and 3D
Matching
Possibilities of 2D and 3D data.
Drawing
Identifying Occupied Parking slots with the help of 3D data.
Drawing final map.

## Slide 53: Matching
Possibilities of the data:

## Slide 54
Matching (continue)

## Slide 55
Drawing

## Slide 56
Map Improvement

## Slide 57: Map Improvement
How can we improved the generated map ?
How can we plot the remaining data or Cars, predicted by our Linear classifier?
  Identify minimum and maximum point of each clusters and draw the rectangles:
Good Choice?

## Slide 58: Map Improvement (Continue)

## Slide 59
Danke Schön